## Slide 1: SMART Home
Group 2:
John Satterla – Computer Engineer – Wireless Connectivity
Zachary Eakerns (Team Lead) – Electrical Engineer – Biomedical Station
Zarka McClung – Computer Engineer – Facial Recognition
Christian Jensen – Electrical Engineer – Voice Recognition

## Slide 2: Last Week's Deliverables
Order and test Zigbee modules
Finalize and start developing with MCU development kits
Zachary Eakerns
John Satterla
Christian Jensen
Zarka McClung
Find software to more accurately simulate filters
Improve filter performance and prepare to construct actual circuits
Research Algorithm and try to implement it
Choose suitable programming language and install IoT on RasPi
Try to use webcam to test Algorithm with detection code
Design and order parts for relay circuit
Research Raspberry Pi Smart home front ends

## Slide 3: Changes From Original Plan
Medical devices, specifically a pulse oximeter, can be high inaccurate due to even small amounts of movement
To get more meaningful, useful data the device will no longer be connected to the person
Instead, a station will be placed in the home that the patient can sit down with and check vitals
This approach emphasizes accuracy over mobility

## Slide 4: Troubles With Filters
Although the values needed to make the amplifiers and filters are simple to calculate, real life results vary heavily from theoretical ones
For the EKG machine the lowpass filter is cutting down on the voltage much quicker than anticipated
While this could still work, fine tuning needs to be done to be able to create a more accurate machine

## Slide 7: Pulse Oximetry Calculations
Blood oxygenation can be calculated by finding the peak voltages given from the phototransistor for both the Red and IR LEDs
Found using the equation
Where

## Slide 8
[6]

## Slide 11: Voice Recognition Methods
Matlab [6]
  Would use the computer and its microphone to detect voice
    Allows for easier integration with the entire project
  Using built-in Matlab functions
    fft() : Fast Fourier transform [4]
    findpeaks(data) : Finds extremes with location vector [5]
Process:
Ask user to set up phrases before
  Type name of phrase
  Speak the phrase (3x times)
  Take the FFT of the signal
  Analyze the highs of the psd
  Save average highs for each word
Speech recognition
  Poll for incoming phrases
  Sample input (fs = ?)
  Take the FFT of the signal
  Analyze the highs of the psd
  Compare with saved averages
*The system will be speaker dependent
(Only recognizing one specific person's commands)

## Slide 12: Voice Recognition Mathematics
Power spectral density equation [9]
Matlab psd graphical example [7]

## Slide 13: System Overview
John Satterla
Wireless Patient Monitor
Room/Space Dimensions TBD
Determines position in Room from BLE Beacons
Sends user data to central processing station for monitoring and web via TBD wireless protocol
Television
Door
Lights throughout
Fan
Facial Recognition/ Voice Command for door and 2 TBD appliance
Central processing station receives and displays data from user and devices
via TBD wireless technology
Bluetooth ToF Beacon
Zigbee Communication

## Slide 14: Controlling Devices Wirelessly with Zigbee
Zigbee is a Wireless, low power mesh networking protocol designed for home and building automation
It supports low data rates (250kbps) and works on top of the defined IEEE 802.15.4 physical layer [16]
The protocol was standardized in 2003 and is maintained by the Zigbee Alliance
Zigbee is probably in most of your homes today, with smart hubs like the Amazon Alexa or Google’s Nest able to connect all devices together
John Satterla

## Slide 15: Controlling Devices Wirelessly with Zigbee
John Satterla
Zigbee Network Topology [16]

## Slide 16: Controlling Devices Wirelessly with Zigbee
John Satterla
For our purposes, we will use Wireless microcontrollers that are integrated into Digi’s “Xbee” modules
[3]
[6]

## Slide 17: Controlling Devices Wirelessly with Zigbee
John Satterla
Using these so that we do not have to do any RF layout with wireless MCUs/ time constraints
Can communicate and be programmed separately for wireless purposes to form network with IDE, and then communicate back to main MCU via SPI or UART
[3]

## Slide 18: Tracking Location of the Patient Monitor
Ideally work indoors, so using GPS not preferred because of accuracy and not able to get fix inside of buildings
BLE ToF – Bluetooth Time of Flight
  Time of Flight is used to estimate range by measuring the round trip delay of an RF packet exchange
  At least two devices needed, and operate generally as a master and a slave, where the master calculates average round trip delay for hundreds of packets to be as accurate as possible (try to reduce error from interference, other RF related differences) [ref]
John Satterla

## Slide 19: Tracking Location of the Patient Monitor
For this, Texas Instruments has a experiential stack that I am going to evaluate and see what kind of performance I can get
The tricky part will be using two masters that are positioned at two known points, and then connecting to the single slave on the patient to triangulate it’s position
[1]
John Satterla
Patient monitor
Master 1
Master 2

## Slide 20: Tracking Location of the Patient Monitor
Hardware on order:
  TI CC2640R2F Launchpads
    Why an SoC? Ability to quickly sample the data coming from the slave and calculate the distance via ToF
    Specs:
      CPU: ARM Core M3 @ 48 MHz
      Memory: 128kB flash, 28kB RAM
      Radio: 2.4GHz with Certified Bluetooth 5, 4.2 support, 102 dB link budget for BLE
      Peripherals: I2C, ISS, UART, TRNG, AES-128
      Low power features: RX at 0dBm – 5.9 mA, TX at +5dBm – 9.1 mA, as low as 1.1uA standby
      General: 3.3V operation
John Satterla

## Slide 21: Blinking LED test using VS and RasPi
Created a simple LED blinking code and connected a LED to Windows 10 IoT Core device. (Raspberry Pi 2 Model B)
Goal was to verify communication between Raspberry Pi and the computer

## Slide 22: Windows 10 IoT with Visual Studio
Connected LED to GPIO 5 (Pin 29) and 3.3V PWR (Pin 1)
Powered it using an adapter
5V (2000mA max)
Connected Ethernet port to transfer data from PC to RasPI
GPIO total output current limit is 100mA

## Slide 23: Assembled circuit
3.3V Supply
300 ohm resistor
Blinks every 500ms

## Slide 24: Demo Video

## Slide 25: Visual studio remote connection setup
Remote machine’s name and IP address was collected using IoT Dashboard

## Slide 26: Code explained
The code for this sample is simple.
We use a timer, and each time the ‘Tick’ event is called, we flip the state of the LED.

## Slide 27: Concept behind the Algorithm
Initially, the algorithm needs a lot of positive images (images of faces) and negative images (images without faces) to train the classifier. Then we need to extract features from it.
Each feature is a single value obtained by subtracting sum of pixels under the white rectangle from sum of pixels under the black rectangle.

## Slide 28: Calculation Method
For each feature calculation, we need to find the sum of the pixels under white and black rectangles.
To solve this, they introduced the integral image. However large your image, it reduces the calculations for a given pixel to an operation involving just four pixels.
It makes things super-fast.
But among all these features we calculated, most of them are irrelevant.
For example, consider the image above. The top row shows two good features. The first feature selected seems to focus on the property that the region of the eyes is often darker than the region of the nose and cheeks.
The second feature selected relies on the property that the eyes are darker than the bridge of the nose. But the same windows applied to cheeks or any other place is irrelevant. So how do we select the best features out of 160000+ features?

## Slide 29: How do we select the best features out of 160000+ features?
For this, we apply each and every feature on all the training images. For each feature, it finds the best threshold which will classify the faces to positive and negative. Obviously, there will be errors or misclassifications. We select the features with minimum error rate, which means they are the features that most accurately classify the face and non-face images.

## Slide 30: Was able to get Microsoft Cognitive Services key for free
The following figure is an example of a LargePersonGroup/PersonGroup named "myfriends“.
Each group may contain up to 1,000,000/10,000 person objects. Meanwhile, each person object can have up to 248 faces registered

## Slide 31: Microsoft Face API Research Phase
Microsoft’s Face API’s algorithm is not shared.
I am using OpenCV to understand how face is recognized (the concept behind it).
Most facial recognition APIs use a similar concept
Microsoft’s API has many of resources
Still debating OpenCV Vs Microsoft Face API

## Slide 32: Gantt Chart

## Slide 33: Gantt Chart

## Slide 34: Budget

## Slide 35: Material Cost

## Slide 36: Next Week's Deliverables
Zachary Eakerns
John Satterla
Christian Jensen
Zarka McClung
Built and begin testing filters
Begin writing and testing software for peak detection
Start sampling input words to find what fs to use
Continue writing Matlab code
Research Matlab controlling MCUs through computer
Keep working on implementing Face recognition code
Research on Face API
Get webcam to test code
Get Zigbee modules and establish communication
Test BLE ToF with launchpads (arriving today)

## Slide 37: References
Cdn-learn.adafruit.com. (2018). [online] Available at: https://cdn-learn.adafruit.com/downloads/pdf/introducing-the-raspberry-pi-2-model-b.pdf [Accessed 3 Oct. 2018].
Dev.ti.com. (2018). Localization Toolbox — SimpleLink™ CC2640R2 BLE-Stack User's Guide for *Bluetooth®* 4.2 3.02.00.00 documentation. [online] Available at: http://dev.ti.com/tirex/content/simplelink_cc2640r2_sdk_2_20_00_49/docs/blestack/ble_user_guide/html/localization/index.html [Accessed 3 Oct. 2018].
“DIGI XBEE® AND DIGI XBEE-PRO® ZIGBEE,” digi.com, 2018. [Online]. Available: https://www.digi.com/pdf/ds_xbee_zigbee.pdf. [Accessed: 25-Sep-2018].
Docs.opencv.org. (2018). OpenCV: Face Detection using Haar Cascades. [online] Available at: https://docs.opencv.org/3.4/d7/d8b/tutorial_py_face_detection.html [Accessed 26 Sep. 2018].
Docs.microsoft.com. (2018). Setting up your device - Windows IoT. [online] Available at: https://docs.microsoft.com/en-us/windows/iot-core/tutorials/quickstarter/devicesetup#using-the-iot-dashboard-raspberry-pi-and-minnowboard [Accessed 3 Oct. 2018].
“EM351/EM357 High-Performance, Integrated ZigBee/802.15.4 System-on-Chip,” silabs.com, 2013. [Online]. Available: https://www.silabs.com/documents/public/data-sheets/EM35x.pdf. [Accessed: 25-Sep-2018].
“fft,” Reconstructing an Image from Projection Data - MATLAB & Simulink Example. [Online]. Available: https://www.mathworks.com/help/matlab/ref/fft.html. [Accessed: 03-Oct-2018].
“findpeaks,” Reconstructing an Image from Projection Data - MATLAB & Simulink Example. [Online]. Available: https://www.mathworks.com/help/signal/ref/findpeaks.html. [Accessed: 03-Oct-2018].
GitHub. (2018). Microsoft/Windows-iotcore-samples. [online] Available at: https://github.com/Microsoft/Windows-iotcore-samples/blob/develop/Samples/HelloBlinky/CS/README.md [Accessed 3 Oct. 2018].
How to Design Peripheral Oxygen Saturation (SpO2) and Optical Heart Rate Monitoring (OHRM) Systems Using the AFE4403, 3AD. [Online]. Available: http://www.ti.com/lit/an/slaa655/slaa655.pdf. [Accessed: 20-Sep-2018].
Mathworks.com. (2018). Power Spectral Density Estimates Using FFT- MATLAB & Simulink. [online] Available at: https://www.mathworks.com/help/signal/ug/power-spectral-density-estimates-using-fft.html [Accessed 3 Oct. 2018].
Ning, D. (2018). Developing an Isolated Word Recognition System in MATLAB. [online] Mathworks.com. Available at: https://www.mathworks.com/company/newsletters/articles/developing-an-isolated-word-recognition-system-in-matlab.html [Accessed 24 Sep. 2018].
“Spectral density,” Wikipedia, 24-Jul-2018. [Online]. Available: https://en.wikipedia.org/wiki/Spectral_density. [Accessed: 03-Oct-2018].
Ti.com. (2018). SIMPLELINK-SDK-VOICE-DETECTION-PLUGIN Voice Detection plug-in for the SimpleLink™ MCU Software Development Kit (SDK) | TI.com. [online] Available at: http://www.ti.com/tool/SIMPLELINK-SDK-VOICE-DETECTION-PLUGIN [Accessed 25 Sep. 2018].
Westus.dev.cognitive.microsoft.com. (2018). Microsoft Cognitive Services. [online] Available at: https://westus.dev.cognitive.microsoft.com/docs/services/563879b61984550e40cbbe8d/operations/563879b61984550f3039523a [Accessed 3 Oct. 2018].
“Zigbee | Overview | Wireless Connectivity,” SimpleLinkTM Zigbee Wireless MCUs, 2018. [Online]. Available: http://www.ti.com/wireless-connectivity/simplelink-solutions/zigbee/overview.html. [Accessed: 26-Sep-2018].

## Slide 38: Questions?